Voltage Loss Calculator for 12 Volt DC Products

When calculating acceptable gauges of wire at specific lengths, you will want to use the table below.  To be safe, round up on the Wattage, and round up on the distance from power supply to the fixture.

Example:  Our Covemax X product is 2 Watts per foot (from the cutsheet), so a 10’ run would use 20 total Watts.  If the distance from the power supply to this 10’ run has to be 50-60’ we consult the table below and find:  20W, 56’ = 18awg wire needed.

Example: Our SMD RGB tape light uses 4.3 Watts per foot (from the cutsheet), so an 8’ run would use 34.4 total Watts (we round up to 40 Watts).  If the distance from the power supply to this 8’ run has to be 45’, we consult the table below and find:  40W, 28’ = 16awg wire needed.

*These Examples are shown in Figure 1 below.

## 12Volt DC or AC Table (3% loss max)

POWER WIRE GAUGE

# W(VA)/Amps   8awg   10awg   12awg   14awg   16awg   18awg   20awg   22awg   24awg   26awg

3W/.25A      3,733  2,396   1,508    947     595     376     234    146     93      59

4W/.33A      2,828  1,815   1,142    717     451     285     177    111     70      44

5W/.42A      2,222  1,426     898    564     354     224     139     87     55      35

10W/.83A     1,124    722     454    285     179     113      71     44     28      18

20W/1.67A      559    359     226    142      89      56      35     22     14       9

30W/2.50A      373    240     151     95      60      38      23     15     N/A     N/A

40W/3.33A      280    180     113     71      45      28      18     11     N/A     N/A

50W/4.17A      224    144      90     57      36      23      14     N/A    N/A     N/A

60W/5.00A      187    120      75     47      30      19      12     N/A    N/A     N/A

70W/5.83A      160    103      65     41      26      16      10     N/A    N/A     N/A

80W/6.67A      140     90      57     35      22      14      N/A    N/A    N/A     N/A

90W/7.50A      124     80      50     32      20      13      N/A    N/A    N/A     N/A

100W/8.33A     112     72      45     28      18      11      N/A    N/A    N/A     N/A

110W/9.17A     102     65      41     26      16      10      N/A    N/A    N/A     N/A

120W/10.00A     93     60      38     24      15      N/A     N/A    N/A    N/A     N/A

*Numbers in Red are in Feet.

Fig. 1  Examples from above.