Voltage Loss Calculator for 24 Volt DC Products

When calculating acceptable gauges of wire at specific lengths, you will want to use the table below.  To be safe, round up on the Wattage, and round up on the distance from power supply to the fixture.

Example:  Our blue LED Neon product is 4 Watts per foot (from the cutsheet), so a 10’ run would use 40 total Watts.  If the distance from the power supply to this 10’ run has to be 70’ we consult the table below and find:  40W, 70’ = 20awg wire needed.

## 24 Volt DC or AC Table (3% loss max)

POWER WIRE GAUGE

# W(VA)/Amps   8awg   10awg   12awg   14awg   16awg   18awg   20awg   22awg   24awg   26awg

3W/.13A     14,417  9,253   5,823   3,656   2,299   1,451    905     565     358    226

4W/.17A     11,025  7,076   4,453   2,796   1,758   1,110    692     432     274    173

5W/.21A      8,925  5,728   3,605   2,263   1,423     898    560     350     222    140

10W/.42A     4,463  2,864   1,803   1,132     712     449    280     175     111     70

20W/.83A     2,258  1,449     912    573      360     227    142      89     56      35

30W/1.25A    1,499    962     606    380      239     151     94      59     37      24

40W/1.67A    1,122    720     453    285      179     113     70      44     28      18

50W/2.08A      901    578     364    229      144      91     57      35     22      14

60W/2.50A      750    481     303    190      120      75     47      29     19      12

70W/2.92A      642    412     259    163      102      65     40      25     16      10

80W/3.33A      563    361     227    143      90       57     35      22     14       9

90W/3.75A      500    321     202    127      80       50     31      20     12       8

100W/4.17A     449    288     182    114      72       45      28     18     11       7

110W/4.58A     409    263     165    104      65       41      26     16     10       6

120W/5.00A     375    241     151     95      60       38      24     15      9       6

130W/5.42A     346    222     140     88      55       35      22     14      9       5

140W/5.83A     321    206     130     82      51       32      20     13      8       5

150W/6.25A     300    192     121     76      48       30      19     12      7       5

160W/6.67A     281    180     114     71      45       28      18     11      7       4

170W/7.08A     265    170     107     67      42       27      17     10      7       4

180W/7.50A     250    160     101     63      40       25      16     10      6       4

190W/7.92A     237    152      96     60      38       24      15      9      6       4

200W/8.33A     225    144      91     57      36       23      14      9      6       4

*Numbers in Red are in Feet.